## Slide 1
WiFi-Enabled Temperature & Humidity Logger with NodeMCU and DHT22
CME 466 – Winter 2025
Prepared by: Alimul Khan, Omid Yaghoobian

## Slide 2
CME 466 Internet of Things
Contents
Getting Started with ESP8266
Reading data from DHT22
Connecting with Internet
IoT with Access Point[On Device IoT]
IoT with Station Mode[Local IoT]
IoT with cloud server [Cloud IoT]
Problem Statement
1

## Slide 3
CME 466 Internet of Things
Problem Statement
This project replaces the Raspberry Pi with a Wi-Fi-enabled NodeMCU ESP8266 to collect sensor data and transmit it to servers for real-time visualization
Block Diagram
2

## Slide 4
CME 466 Internet of Things
Objective
IoT Systems with ESP8266
Display data on serial monitor
Communicate both way using any browser
NodeMCU+ DHT22
The objective of this project is to develop an IoT system using ESP8266 and DHT22 sensor to collect temperature and humidity data, display it on the Serial Monitor, and send it to a remote server for real-time monitoring.
The project explores various communication methods and library options for efficient data handling.
3

## Slide 5
CME 466 Internet of Things
Node MCU
Widely used microcontroller
Programmable on the shelf WiFi chip
esp8266
Temperature: -40 to 80 ºC +/-0.5ºC
Humidity: 0 to 100% +/-2%
4

## Slide 6
CME 466 Internet of Things
NodeMCU ESP8266 Microcontroller Pinout
5

## Slide 7
CME 466 Internet of Things
DHT22 Sensor Pinout
6

## Slide 8
CME 466 Internet of Things
How to connect the DHT22 to the ESP8266 Microcontroller
ESP8266 Module
DHT22 Sensor
Breadboard
Jumper wires
Data
7

## Slide 9
CME 466 Internet of Things
IoT Systems with ESP8266
Getting Started with ESP8266
Blink:
Go ahead with pdf provided
Just Warmup
8

## Slide 10
CME 466 Internet of Things
IoT Systems with ESP8266
Reading data from DHT22
Install DHT22 library
Use this example to see sensor data at the serial terminal
See its library examples for more details
Include libraries
Define pins and sensor types
Initialization of DHT variable
Initialization of temperature and humidity
9

## Slide 11
CME 466 Internet of Things
IoT Systems with ESP8266
Reading data from DHT22
Reading sensor data
For testing only:
If the DHT22 sensor is not connected, the code will send fake (hardcoded) sensor data.
‘isnan’ function is used to check if the received string is not a number.
10

## Slide 12
CME 466 Internet of Things
IoT Systems with ESP8266
Reading data from DHT22
Initialized serial communication and dht22 sensor. Make sure the baud rate is same as Serial.begin(115200);
Sending formatted data over serial communication
Reading the temperature by calling getTempHumidity();
11

## Slide 13
CME 466 Internet of Things
IoT Systems with ESP8266
Reading data from DHT22
espDHT22
Open the serial terminal.
Ensure the correct baud rate is selected.
Try reconnecting the sensor if the reading fails.
12

## Slide 14
CME 466 Internet of Things
IoT Systems with ESP8266
ESP internet Connection Modes
Most Common Modes:
Access Point (AP) Mode: The ESP creates its own Wi-Fi network, allowing other devices to connect.
Station (STA) Mode: The ESP connects to an existing Wi-Fi network as a client.
Cloud Mode: The ESP connects to a cloud server over the internet for remote access and data exchange.
13

## Slide 15
CME 466 Internet of Things
IoT Systems with ESP8266
ESP Access Point
Organizing Code with Modules:
The whole code is modularized into multiple .h and .cpp files alongside main.ino for better organization and maintainability.
14

## Slide 16
CME 466 Internet of Things
IoT Systems with ESP8266
ESP Access Point
Use a specific SSID and password to connect to the Access Point, then browse to 192.168.4.1.
15

## Slide 17
CME 466 Internet of Things
IoT Systems with ESP8266
ESP Station Mode
Access Point Mode
Station Mode
Station Mode:
WiFi.begin(ssid, password);
Serial.print("Connecting to WiFi ");
while (WiFi.status() != WL_CONNECTED) {
delay(1000);
Serial.print(".");
}
AP mode:
WiFi.softAP(ssid, password);
16

## Slide 18
CME 466 Internet of Things
IoT Systems with ESP8266
ESP cloud more
Key features:
Node sends data only when requested by the user.
Data transmission is triggered upon receiving a valid request.
Users can view real-time sensor data through the web interface.
Reduces unnecessary data transfer and conserves bandwidth.
This project uses an ESP8266 with a DHT22 sensor to measure temperature and humidity, with a Python Flask-based server on a computer acting as the cloud. Users access their node using a unique chip ID, and data is sent only upon request for efficient, on-demand communication.
17

## Slide 19
CME 466 Internet of Things
IoT Systems with ESP8266
ESP cloud more
esp part
Server part
There are three files in this directory
espCloud.ino
SensorData.h
SensorData.cpp
There are four files in this directory
get_local_ip.py
espCloudApp.py
templates/node.html
static/style.css
18

## Slide 20
CME 466 Internet of Things
IoT Systems with ESP8266
ESP cloud more
6. Browse from a device on same network: http://127.0.0.1:5000/node/chipID
2. Replace serverIP here in espCloud.ino:
const char* serverIP = "10.0.0.181";
3. Connect HW with computer and load Arduino code
1. Run “get_local_ip.py” and get your IP in the terminal, let say it is 10.0.0.181
4. Note the link you are supposed to browse along with chip ID from the serial terminal: http://127.0.0.1:5000/node/chipID or http://10.0.0.181:5000/node/chipID
5. Run espCloudApp.py
7. Send Desired command to get data from your sensor
19

## Slide 21
CME 466 Internet of Things
IoT Systems with ESP8266
ESP cloud more
20
Run get_local_ip.py
Replace IP in *.ino
Upload firmware
Find the link

## Slide 22
CME 466 Internet of Things
IoT Systems with ESP8266
ESP cloud more
or
21
Browse Now